## Slide 1
RAJAMAHENDRI INSTITUTE OF ENGINEERING AND TECCHNOLOGY
ELECTRONICS AND COMMUNICATION ENGINEERING
Under the Guidance of
Dr. CH. SURYABABU,
M.Tech, Ph.D.
PRESENTED BY: J. DHEERAJ 21MD1A0429
G. BHARATH CHANDU 21MD1A0422
N. SATISH CHANDRA 22MD5A0407
M. JAGADIESHESWAR 21MD1A0440

## Slide 2
TITLE
Mean Based Approach To Omnidirectional Pathfinding Algorithm Using Single Ultrasonic Sensor for Robotic Car

## Slide 3
Contents
Abstract
Introduction
Problem statement & challenges
System components
Working mechanism
Block diagram
Existing methods & limitations
Proposed method
Advantages and future scope

## Slide 4
Abstract
We propose an IoT-enabled omnidirectional pathfinding system to improve real-time obstacle detection and navigation for autonomous robotic vehicles. By integrating a single ultrasonic sensor, a servo motor, L293D motor driver, and IoT-based monitoring, our system scans a 180-degree field for better detection and accuracy. Processed data from the sensor allows smooth navigation via a mean-based pathfinding algorithm. This system reduces false positives, optimizes movement, and enables remote monitoring, ideal for applications like search-and-rescue, industrial automation, and hazardous environment exploration.

## Slide 5
Introduction
Pathfinding algorithms are crucial in robotics and automation for finding paths and avoiding obstacles.
Existing pathfinding algorithms for ultrasonic sensors are limited by their monodirectional nature, often relying on simple binary decisions (left and right), leading to inaccuracies.
Enhancements to these algorithms aim to improve their accuracy.
These algorithms have applications in the military to reach inaccessible or dangerous areas.

## Slide 6
Problem Statement & Challenges
Problem Statement:
In modern robotics and automation, the accuracy and efficiency of pathfinding algorithms are limited by the monodirectional nature of ultrasonic sensors
Often rely on simple binary directional decisions (left and right).
inaccuracies in pathfinding and obstacle avoidance,
Challenges:
Real-time Processing.
Algorithm Enhancement.
Environmental Adaptation.
Reduce false Alarms.

## Slide 7
System Components
Arduino Uno
L293D Motor Driver
Chassis
Motor & wheels
Ultrasonic Sensor HC-SR04
Servo motor
Jumper wires

## Slide 8
System Components
Arduino Uno
L293D Motor Driver
Chassis
Motor & wheels
Ultrasonic Sensor HC-SR04
Servo motor
Jumper wires

## Slide 9
System Components
1. Arduino Uno
Digital Pins (D0 – D13)
Analog Pins (A0 – A5)
Power pins
  Vin , 3.3v,5v,ioref,reset
Processor: Atmega328P
PWM pins: 3,5,6 , 9,10,11
UART PINS: D0,D1

## Slide 10
System Components
2. L293D Motor Driver
The L293D is a popular motor driver IC used to control the direction and speed of DC motors. It contains two H-bridge circuits, allowing it to control two DC motors simultaneously

## Slide 11
System Components
3. Chassis
The chassis is the structural framework of a vehicle, providing support for all other components, including the body, engine, and wheels. It ensures stability and strength, allowing the vehicle to function properly.

## Slide 12
System Components
4. servo Motor
A servo motor is a rotary actuator that allows for precise control of angular position, velocity, and acceleration. It consists of a motor, a position sensor, and a control circuit. Servo motors are commonly used in robotics, automation, and control systems to perform tasks requiring precise positioning.

## Slide 13
System Components
5. Ultra Sonic Sensor HC-SR104
An ultrasonic sensor measures distance by emitting sound waves and timing the returning echo. It's commonly used in robotics, automation, and vehicles for detecting obstacles and measuring distances.
Specification:
Operating voltage: 5V
Frequency : 40KHz
Measuring range: 2cm to 400cm

## Slide 14
System Components
6. Jumper Wires
Jumper wires are flexible connectors with pins at each end, used to link components on breadboards or prototyping tools. Available in various lengths and colors, they simplify circuit creation and testing, making them essential for quick prototyping.

## Slide 15
Working Mechanism
Normal Detection Method:
  Utilizes an ultrasonic sensor to measure the distance between the car and the nearest object in its line of sight.
  This method is not omnidirectional, meaning it only detects objects directly in front of the sensor.
  Most commonly used and does not involve the use of a servo motor
Intensive Detection Method:
  Employs a servo motor to rotate the ultrasonic sensor, providing a 180-degree view for omnidirectional detection
  Sensor starts at 0 degrees (extreme left) and rotates to 180 degrees (extreme right) in 3-degree steps
  Collected data is analyzed to determine the subsequent actions

## Slide 16
Block Diagram
Ultrasonic Sensor
Power supply
16*2 LCD
Servo motor
L293D motor driver
M1
M2
Arduino Uno

## Slide 17
Interfacing of Components
Transformer
12-0-12
Base Board
Power supply board
Arduino uno
Pin

## Slide 18
Existing Methods & Limitations
Static ultrasonic sensors provide monodirectional obstacle detection, leading to blind spots and inefficiencies in complex environments.
Signal reflections cause inaccurate readings, requiring frequent path recalculations
Lack of servo motor-driven scanning limits adaptive obstacle detection capabilities.
Absence of motor control mechanisms (e.g., L293D driver) results in imprecise movement and inefficient navigation.

## Slide 19
Proposed Method
The system integrates an ultrasonic sensor mounted on a servo motor for 180° scanning, improving obstacle detection.
A mean-based algorithm processes the data, reducing false positives and optimizing path selection.
The L293D motor driver ensures precise control of the robot's movements.
Enhanced navigation makes it suitable for industrial, rescue, and autonomous applications.
This approach provides better accuracy and efficiency compared to traditional systems.

## Slide 20
Advantages & Future Scope
Advantage:
Enhanced Mobility
Time Efficiency
Efficient Pathfinding
Energy Efficiency
Future Scopes:
Disaster Response
Smart Vehicles
Space Exploration